## Slide 1
module decoder ( input [2:0] a, output reg [7:0] y);
always @(*)
case (a)
3’b000: y <= 8’b00000001;
3’b001: y <= 8’b00000010;
3’b010: y <= 8’b00000100;
3’b011: y <= 8’b00001000;
3’b100: y <= 8’b00010000;
3’b101: y <= 8’b00100000;
3’b110: y <= 8’b01000000;
3’b111: y <= 8’b10000000;
endcase
endmodule
3:8 decoder using case

## Slide 2
What device does the following Verilog code represent?
always @(CLK, Clr, Set) begin if(Clr == 1'b1) Q <= 1'b0; else if(Set == 1'b1) Q <= 1'b1; else if(CLK == 1'b0) Q <= D; else begin end end

## Slide 3
always begin wait(E); A <= #5 1; B <= A + 1; C <= #10 B; D <= #3 B; A <= #15 A + 5; B <= B + 7; end
In the following Verilog process A, B, C, and D are all registers that have a value of 0 at time=10 ns. If E changes from 0 to 1 at time = 20ns, specify the time(s) at which each signal will change and the value to which it will change. List these changes in chronological order.

## Slide 5
reg [7:0] C; reg signed [7:0] D; reg signed [7:0] A = 8'hD5;
evaluate i. C = A >> 4 ii. C = A >>> 4 iii. C = A << 4 iv. C = A <<< 4 v. D = A >> 4 vi. D = A >>> 4 vii. D = A << 4 viii. D = A <<< 4
A= 11010101

## Slide 6
Assume D1=0, D2=5, and D1 changes to 1 at time=10 ns. What are the values of D1 and D2 after the following code has been executed once? Do the values of D1 and D2 swap?
always @ (D1)
begin
D2 <= D1;
D1 <= D2;
End

## Slide 7
If A 5 101, B 5 011, and C 5 010, what are the values of the following statements? Assume A, B, and C are of reg type. Assume as many bits as necessary for the result.
(a) {A,B} | {B,C} (b) A >> 2 (c) A >>> 2 (d) {A,(~B)} == 111110 (e) A | B & C

## Slide 8
module Question(input wire CLK, output reg [31:0] OUT);
initial
OUT <= 0;
always @(posedge CLK)
OUT <= OUT + 1;
endmodule
Which system?

## Slide 9
A description of a 74194 4-bit bidirectional shift register follows. The CLRb input is asynchronous and active low and overrides all the other control inputs. All other state changes occur following the rising edge of the clock. If the control inputs S1 = S0 = 1, the register is loaded in parallel. If S1 = 1 and S0 = 0, the register is shifted right and SDR (serial data right) is shifted into Q3. If S1 = 0
and S0 = 1, the register is shifted left and SDL is shifted into Q0. If S1 = S0 = 0, no action occurs

## Slide 10
`define TICK #2
module downCntr(clk, reset, Q);
input clk, reset;
output [3:0] Q;
reg [3:0] Q;
always @ (posedge clk)
begin
if (~reset) begin
Q <= `TICK Q-1;
end
end
always @ (posedge reset)
begin
Q <= 4'b0000;
end
endmodule
Down Counter